## Slide 1
EV Design
Master Class Series

## Slide 2: Introduction to EV

## Slide 3: Conventional Vehicles

## Slide 4: Hybrid Electric Vehicles
Ideal Start – Stop System
Ideal Start – Stop, Break Energy Regeneration, Torque assistance during Acceleration
Full Electric Drive
Autonomous Electric Vehicle

## Slide 5: Electric Vehicle

## Slide 6: Pros & Cons
Charging station
Range of Distance
Temperature
Lower Maintanance
Simple Control
Limittations
Cost
Lack of Conventional Fuel
Option to utilize Renewable Energy
Environmental
Less no of Power Conversion
Energy Efficiency

## Slide 7: Electric Vehicle Components
Battery, Motor, PCU
Motor, Battery, Power Control Unit, Onboard Charger
02
Vehicle Structure
Wheel, Vehicle Body, Gear
01
Assembley
Other Essential Components
03

## Slide 8: EV Parts
Body
Motor
Inverter
Battery Bank
On Board Charger
Charging Station

## Slide 9: Block Diagram
Battery
Vehicle Body
Motor
Motor Controller
Control Signal

## Slide 10: Vehicle Design Procedure
Propulsion power
Motor Size
Battery Capacity

## Slide 11: Vehicle Basics
Push Force
Friction Force

## Slide 12: Power Required to move vehicle
Power = Total Tractive Force x Velocity of the vehicle
Push Force
Friction Force
Gravitational Force
Aerodynamic Drag Force
Free Body Diagram

## Slide 13: Forces on the Vehicle
Total Tractive Force
Rolling Resistance Force(Frr)
Aerodynamic drag force(Faero)
Hill climbing Force(Fhc)
Acceleration Force(Fxi)
    Linear Acceleration Force
    Angular acceleration force

## Slide 14: Rolling Resistance Force
Car tires on Concrete/asphalt 0.013
Car tires on rolled gravel 0.02
Tar Macadam 0.025
Unpaved Road 0.05
Field 0.1 - 0.35
Truck Tires on concrete or asphalt 0.006 - 0.01
Wheels on Rail 0.001 - 0.002
It is one of the forces that act to oppose the motion of a vehicle
The Coefficient, is a function of the Tire material, structure, temp, pressure, tread geometry, road roughness, material, presence & absence of liquids on the road.
This value varies with SPEED.
Tire pressure increases its value decreases
Frr = µrr m.g
µrr - Rolling Resistance Constant
m - Mass of the Vehicle
g - Gravitational acceleration constant

## Slide 15: Aerodynamic Drag Force
The force on an object that resists its motion through a air is called drag.
Drag is a force that acts parallel to and in the same direction as the airflow.
Aerodynamic drag increases with the square of speed.
Fad = ½ρCdAv2 Newtons
ρ – Air Density kg/m3
A – Frontal Area m2
Cd – Drag Coefficient
v - Velocity of the Vehicle m/s
High Pressure
Low Pressure
Moving Direction

## Slide 16: Drag Coefficient constan Typical Values
Trucks Road Trains 0.8 - 1.5
Buses 0.6 - 0.7
Modified Buses/car 0.3 - 0.4
Motorcycles 0.6 - 0.7

## Slide 17: Hill Climbing Force
Rise / Run
Fhc = m.g.Sin θ
Run
Rise
Length
θ

## Slide 18: Acceleration Force
Linear Acceleration force (Fla) = m.a
Angular Acceleration force (Fωa)
I - moment of inertia
G – Gear Ratio
a - Acceleration
r – Radius of tire
- Efficiency of gear

## Slide 19: Total Power Required
Total Power P = Fte . v
Fte Total Tractive Power = Frr + Fad + Fhc + Fla + Fwa
Frr - Rolling Resistance Force
Fad – Aerodynamic Drag Force
Fhc - Hill Climbing Force
Fla - Linear Acceleration Force
Fwa - Angular Acceleration Force
Frr = µrr m.g
µrr - Rolling Resistance Constant
m - Mass of the Vehicle
g - Gravitational acceleration constant
Fad = ½ρCdAv2 Newtons
Fhc = m.g.Sin θ
(Fla) = m.a
ρ – Air Density kg/m3
A – Frontal Area m2
Cd – Drag Coefficient
v - Velocity of the Vehicle m/s
Hill Climbing Force
Aerodynamic Drag Force
Rolling Resistance Force
Linear Acceleration Force
Angular Acceleration Force
I - moment of inertia
G – Gear Ratio
a - Acceleration
r – Radius of tire
- Efficiency of gear

## Slide 20: EV Rating(2w)
Parameters | Notations | Value | Units
Weight | m | 1,000.00 | Kg
Width | W | 1.00 | m
Hieght | H | 1.50 | m
Rolling Resistance | µrr | 0.02 | 
Air Density | ƥ | 1.25 | kg/m2
Drag Coefficient | Cd | 0.30 | 
gravitational Force | g | 9.80 | 
Speed in km |  | 40.00 | kpmh
Frontal Area | A | 1.50 | m2
Velocity | v | 11.11 | m/sec
Tractive Force | Fte | 170.15 | Nm
Total Power for 40Km | P | 1,890.53 | Watts
Total Power = Total Tractive Force x Velocity
Velocity = kpm -> m/s
= 40 * 1000/3600
Tractive Force = Rolling Resistance Force +
Aerodynamic drag force
Total Power P = Fte . v
Fte (Total Tractive Power) = Frr + Fad

## Slide 21: Power x Speed of EV

## Slide 22: Sample Data
rider_mass = 80 kg
vehicle_mass = 237 kg
CG_height = 254 mm
drag_coeff = 1.2
front_axle = 1520 mm
rear_axle = 1400 mm
front_area = 1.33 m2
Tire Parameters
tire_b = 10
tire_c = 1.9
tire_d = 1
tire_e = 0.97
tire_dia = 18 inch
tire_inertia = 1e-3 kg*m2
roll_resist = 0.005

## Slide 23: MATLAB

## Slide 24: Example
Basic Vehicle Modeling